## Slide 1: Routing in Ad Hoc Networks

## Slide 2: Ad Hoc Network
Is a network which is built spontaneously as devices connect
Does not rely on base station to coordinate flow of messages to each node. Nodes forward packets to and fro from each other
Here, node is mobile. Unlike in Mobile Hosts only hosts are mobile

## Slide 3: Ad Hoc Network
No fixed topology
No fixed neighbour
No known neighbour
Topology changes all the time  validity of paths changes spontaneously

## Slide 4: Types of routing algorithms in Ad Hoc network
Proactive
  Periodically
Reactive
  Only when needed
Hybrid
  Combination

## Slide 5: AODV
Adhoc On Demand Distance Vector
Find a path from source to destination only when needed and maintains it for as long as it needs
Advantage
  Accounts to limited bandwidth and low battery life
  Low overhead
Disadvantage
  Large delay from the moment route needed to the moment route is acquired

## Slide 6: AODV – 2 major tasks
ROUTE DISCOVERY
ROUTE MAINTENANCE

## Slide 7: AODV - Example
S
A
B
C
D
<destination, next hop, destination seq no, lifetime>

## Slide 8: AODV
Objective – find the path from Source(S) to Destination(D)
Solution-
  S looks in its table for an entry to D
  Check for entry
    (a) If gets an entry send packet
    (b) Else ROUTE DISCOVERY process starts

## Slide 9: ROUTE DISCOVERY
S creates ROUTEREQUEST packet and broadcasts it to its neighbour A
A looks in its local history table to see if request has already been seen and processed
  If duplicate – reject request
  Else – enter req. in this table
A looks in its route table for path to D
  No path to D, so rebroadcasts to its neighbours B and C
  Store in reverse route table
C on receiving the broadcast has 2 options
  C sends REPLY to D about the path, or,
  C broadcasts to D and D sends REPLY
D creates ROUTEREPLY packet and unicasts to S
  Intermediate path nodes inspects ROUTEREPLY and makes entry in their table

## Slide 10: ROUTE MAINTENANCE
Topology keeps changing
Each node broadcasts HELLO packet to its neighbours
Neighbours respond to it
If a node X do not respond to HELLO packet implies node no longer in the network
  Broadcaster node looks in its table and informs its active neighbours
  All these nodes will further clear the paths using X
  These active neighbours will in turn inform their active neighbours until node X is cleared from all routing tables
Active Neighbours = During last t sec, neighbour nodes that got a packet for sender to destination X
Source S ------- Destination X
  Active neighbours of S : all nodes that helped to get packet to reach X

## Slide 11: Example
A
B
D
F
C
E
G
H
I
D’ s routing table
Dest. | Next Hop
A | A
B | B
C | B
E | G
F | F
G | G
H | F
I | G

## Slide 12
A
B
D
F
C
E
G
H
I
D’ s routing table
A to I -- not available
Dest. | Next Hop
A | A
B | B
C | B
E | G
F | F
G | G
H | F
I | G

## Slide 13
A
B
D
F
C
E
H
I
Dest. | Next Hop
A | A
B | B
C | B
E | G
F | F
G | G
H | F
I | G
D’ s routing table
A to I -- not available
I’ s active neighbours A, B
D sees E,G,I uses G