## Slide 1: Closed loop solutions

## Slide 2: Monitor
Detect when and where congestion occurs
Metrics used –
  % of all packets discarded for lack of buffer space
  Average queue length
  Number of packets that time out and retransmitted
  Average packet delay
  Standard deviation of packet delay
Higher the metric value  growing congestion

## Slide 3: Pass information
Inform to places where action can be taken
Pass the information of congestion from the point of detection to the point of correction
Ways
  Packet –
    Router that detects congestion sends packets to traffic source(s) announcing problem.
    Leads to further congestion
  Bit/Field –
    a field is reserved in packet to be set by router when congestion crosses threshold. Router sets this field in all outgoing packets to warn
  Probe packet –
    Hosts and routers periodically send these to explicitly ask about congestion
    This information can be used to route traffic around problem area

## Slide 4: References
https://en.wikipedia.org/wiki/Network_congestion
http://www.linfo.org/congestion.html