## Slide 1: Congestion

## Slide 2: Congestion
When number of packets dumped into subnet is more than its carrying capacity.
When too many packets are in the subnet performance degrades
Network congestion is the situation in which an increase in data transmissions results in a proportionately smaller increase, or even a reduction, in throughput.
Network congestion in data networking and queuing theory is the reduced quality of service that occurs when a network node is carrying more data than it can handle.
Congestion results from applications sending more data than the network devices (e.g., routers and switches) can accommodate, thus causing the buffers on such devices to fill up and possibly overflow.

## Slide 3: Causes of Congestion – 1/3
Memory
Example - Packets arriving in 3 lines and all need same output line queue will be made if insufficient memory to hold packets  packets lost
If increase memory  problem worsens
Since, packets time out leading to retransmission  increase in load

## Slide 4: Causes of Congestion – 2/3
2) Slow Processor
Line capacity is good but processing is slow  queues build up

## Slide 5: Causes of Congestion – 3/3
3) Low bandwidth
Upgrading part and not all simply shifts the bottle neck elsewhere
If bandwidth is high, processor is low  congestion
If bandwidth is low, processor is high  congestion

## Slide 6: General Principles of Congestion Control
Congestion Control
Preventive Policy
Corrective Policy
Solve the problem by good design
No mid course corrections
Tools
Acceptance of new traffic?
Rejection of packets?
Schedules ?
3 parts
Monitor
Pass
Adjust
No Regard to current state of the network
Regards to current state of the network

## Slide 7: Corrective Policy

## Slide 8: Monitor
Detect when and where congestion occurs
Metrics used –
  % of all packets discarded for lack of buffer space
  Average queue length
  Number of packets that time out and retransmitted
  Average packet delay
  Standard deviation of packet delay
Higher the metric value  growing congestion

## Slide 9: Pass information
Inform to places where action can be taken
Pass the information of congestion from the point of detection to the point of correction
Ways
  Packet –
    Router that detects congestion sends packets to traffic source(s) announcing problem.
    Leads to further congestion
  Bit/Field –
    a field is reserved in packet to be set by router when congestion crosses threshold. Router sets this field in all outgoing packets to warn
  Probe packet –
    Hosts and routers periodically send these to explicitly ask about congestion
    This information can be used to route traffic around problem area

## Slide 10: References
https://en.wikipedia.org/wiki/Network_congestion
http://www.linfo.org/congestion.html