## Slide 1: Internet Transport Protocol - UDP

## Slide 2: UDP
User Datagram Protocol
Connection less
Unreliable
No flow control
No error control
No congestion control

## Slide 3: UDP header fields
Source Port
Destination Port
UDP Length
  Length of the datagram (header size + payload size)
UDP Checksum

## Slide 4: Remote Procedure Call - RPC

## Slide 5: Steps in making a remote procedure call
The idea behind RPC is to make a remote procedure call look as much as possible
like a local one

## Slide 6: RPC
Client program must be bound with a small library procedure, called the client stub. It represents the server procedure in the client’s address space
Server is bound with a procedure called the server stub
These procedures hide the fact that the procedure call from the client to the server is not local

## Slide 7: Steps in RPC
STEP 1 – client calling the client stub. Parameters pushed onto the stack in the normal way
STEP 2 - client stub packing the parameters (marshaling) into a message and making a system call to send the message
STEP 3 - operating system sending the message from the client machine to the server machine
STEP 4 – operating system passing the incoming packet to the server stub
STEP 5 – server stub calling the server procedure with the unmarshaled parameters
The reply traces the same path in the other direction

## Slide 8: Real Time Transport Protocol

## Slide 9: Application Area
Real time multimedia applications –
  Internet radio
  Internet telephony
  Music –on-demand
  Video –on-demand
  Videoconferencing

## Slide 10: Where does RTP belong ?
RTP is a transport protocol implemented in Application Layer

## Slide 11: Basic Function of RTP
Multiplex several real time data streams onto single stream of UDP data units

## Slide 12: RTP
Does not perform/have the following –
Flow control
Error control
Mechanisms to request retransmissions
Acknowledgements

## Slide 13: RTP Header

## Slide 14: Fields of RTP Header