## Slide 1
Comparison
of Different
Network Topologies
Presentation by:
Wanbok G. Thabah
Roll No. 19

## Slide 2: Points of comparison
Setup
Transmission Method
Expansion
Cost
Cabling Concern
Reliability
Response Time

## Slide 3: Setup
Bus | Connect the cable from one computer to the next and so on to the end. A terminator is placed at each end of the network.
Star | Each computer must be close to the central device.100 meters maximum cable length, up to 24 computers per network
Ring | Computers are located close to each other. Setup is easy. The ring has no beginning and no end.
Mesh | There are at least two nodes with two or more paths between them.
Hybrid | Often created when expanding an existing network. Can use a variety of connection devices
Tree | The tree layout begins at a point known as the head end(Root), where one or more cables start, and each of these may have branches. The branches in turn may have additional branches to allow quite complex layouts

## Slide 4: Transmission method
Bus | One computer at a time sends information. Information goes along the cable and the computer accesses the information off the cable.
Star | All information passes through the central network connection
Ring | One method of transmitting data around a ring is called token passing. The token is passed from computer to computer until it gets to a computer that has data to send.
Mesh | Uses routing or flooding.
Hybrid | Transmission can happen in different ways, depending on the other topologies.
Tree | a transmission from any station propagates throughout the medium and can be received by all other stations.

## Slide 6
Mesh Topology
Tree Topology
Hybrid Topology

## Slide 7: Expansion
Bus | Upon expanding the network, a barrel connector is used to join two cables.
Star | Add a new computer by plugging in a new cable from the computer to the connection device.
Ring | Cable between the computers must be broken to add a new computer, so the network is down until the new device is back online.
Mesh | To add a new computer, a link have to be laid to each of the existing computer.
Hybrid | Connection devices make combining different networks and different topologies easy.
Tree | The simplest to install and extend extra stations in a daisy chain manner.

## Slide 8: Cost
Bus | A cheaper network since there is usually one continuous copper cable.
Star | More expensive of the simple topologies, it requires costly connection device.
Ring | Fairly low.
Mesh | Expensive, large, and usually complicated.
Hybrid | Costly Hubs and infrastructure.
Tree | Costly because it is heavily cabled.

## Slide 9: Cabling Concern
Bus | Single continuous cable connects the devices. Terminator is required at each end of the cable. Uses coaxial or twisted pair cabling.
Star | Uses twisted pair cable. Requires large amounts of cable. No more than 100 meters from the computer to the connection device
Ring | Requires more cabling than other topologies. Uses twisted pair.
Mesh | twisted pair, coaxial or fiber.
Hybrid | Cabling depends on the types of networks. twisted pair, coaxial or fiber.
Tree | Overall length of each segment is limited by the type of cabling used.(Coaxial– Twisted Pair – Fiber)

## Slide 10: Reliability
Bus | If cable malfunctions, the entire network goes down.
Star | When one computer goes down, the rest of the network is unaffected. If the connection device goes down, then the network is down.
Ring | If there's a break in the cable or an error in the network, information continues to transfer through the rest of the ring until reaching the point of the break.
Mesh | Allows communication to continue in the event of a break in any connection.
Hybrid | Troubleshooting is easy in this network, the part in which fault is detected can be isolated from the rest of the network.
Tree | If a node fails, the connection is isolated and information can continue onwards.

## Slide 11: Response Time
Bus | Delay cause broadcast.
Star | Excellent in terms of distance.
Ring | Good.
Mesh | Trade off with cost.
Hybrid | The worst.
Tree | Possible traffic jams.

## Slide 12
Thank You