## Slide 1: Solutions
Different policies at different layers and their effect to congestion
Data Link Layer
  Retransmission policy
  Out of order caching
  Acknowledgement policy
  Flow control
Network Layer
  Virtual circuits vs Datagram inside subnet
  Packet queuing and service policy
  Packet discard policy
  Routing algorithm
  Packet lifetime management
Transport Layer
  Retransmission policy
  Out of order caching
  Acknowledgement policy
  Flow control
  Timeout determination

## Slide 2: Corrective Policies

## Slide 3: Congestion Control in virtual circuit subnets
Admission Control
  Once congestion detected no more new v.c setup
Allow new virtual circuit
  Carefully route all v.c around problem area
Negotiation
  Negotiate an agreement between host and subnet when v.c set up
  Guarantees no congestion since resources are reserved and hence available
  Performed
    All the time
    Only when congestion occurs

## Slide 4: Congestion Control in Datagram Subnets
Signal that congestion has occurred by monitoring
  Line utilization
  Buffer utilization
  Queue length etc.
Routers can monitor utilization of all its output lines and other resources
  Associate a real variable which reflects if certain threshold is crossed or not. On crossing the threshold output line is set to “warning set”

## Slide 5
When packets arrive at routers in such situation either of 3 actions:
Warning bit
Choke packets
Hop by Hop choke packets

## Slide 6: Warning Bit
S
A
B
D

## Slide 7: Warning Bit
S
A
B
D

## Slide 8
Congestion at B
B detects congestion and sets warning bit in packet’s header
Packet reaches destination
Destination’s transport entity copy warning bit to ack. Sent back to source
Source then cuts back traffic
As long as router is in warning state continues setting warning bit
  Source monitors ack. With bit set and adjust transmission rate accordingly
  When ack. Is normal traffic is increased
Destination informs about congestion to source via ack.

## Slide 9: Choke Packet
Router informs source about congestion via choke packets
S
A
B
D

## Slide 10
Congestion at A
A sends
  Choke packet to source
  Tags header bit of the original packet
    Same packet will not generate choke packets again in other router
Source then reduces the traffic to destination by X% for a time interval.
Source will further listen for more choke packets. If choke pkt. arrives traffic is further reduced (or increased accordingly)
Choke packet can contain mild/stern/ultimatum warning

## Slide 11: Hop by Hop Choke packets
Intermediate routers inform about congestion
A
B
E
F
C
D

## Slide 12
Router A to router D = transmission
Congestion at D
Choke packet reaches F
F reduces flow to D (immediate relief to D )
Choke reaches E, E reduces flow to F
Choke reaches A, A reduces flow to E, relief to E
Router informs and relays choke and at each hop relief is given to D