## Slide 1: Linkers

## Slide 2: Introduction
Execution of a program written in a language involves
  Translation of the program : translator for language
  Linking of the program with other programs needed for its execution : linker
  Relocation of program to execute from the specific memory area allocated to it : linker
  Loading of the program in memory for the purpose of execution : loader

## Slide 3: Introduction (cont..)
Translator outputs a program form called object module for the program
Linker processes a set of object modules to produce ready-to-execute program form called binary program
Loader loads this program into memory for the purpose of execution

## Slide 4
translator
linker
loader
Binary pgm
Data flow
Control flow
Binary
pgms
Object
modules
Source
pgm
Data
results
Fig : Program execution

## Slide 5: Translated, linked and load time address
While compiling a program P, a translator is given an origin specification for P – translated origin of P
Translator uses the value of the translated origin to perform memory allocation for the symbols declared in P
This results in assignment of translation time address tsymb to each symbol symb in the program
The execution start address (start address) of a program is the address of instruction from which its execution must begin

## Slide 6: Translated, linked and load time address (cont..)
The start address specified by the translator is the translated start address of the program
Origin of a program have to be changed by linker or loader for one of two reasons
  The same set of translated addresses may have been used in different object modules constituting a program. Memory allocation to such programs would conflict unless their origins are changed

## Slide 7: Translated, linked and load time address (cont..)
  An OS may require that a program should execute from a specific area of memory. This may require a change in its origin. Change of origin leads to changes in execution start address and in the addresses assigned to symbols

## Slide 8
Terminology referring to address of program entity at different types
  Translation time (or translated) address : address assigned by translator
  Linked address : address assigned by linker
  Load time (or load) address : address assigned by loader

## Slide 9: Translated, linked and load time address (cont..)
Translated time, linked time and load time are used with the origin and execution start address of a program
  Translated origin : Address of the origin assumed by the translator. This is the address specified by the programmer in ORIGIN statement
  Linked origin : Address of the origin assigned by linker while producing a binary program
  Load origin : Address of origin assigned by loader while loading the program for execution
Linked and load origin may differ from translated origin of program

## Slide 10: Program relocation (cont..)
Address sensitive program P can execute correctly only if the start address of memory area allocated to it is the same as its translated origin
For executing correctly from other memory area, address used in each address sensitive instruction of P must be ‘corrected’

## Slide 11: Program relocation (cont..)
Program relocation is the process of modifying the addresses used in the address sensitive instructions of a program s.t. the program can execute correctly from designated memory area
If linked origin ≠ translated origin
  Relocation is performed by linker
If load origin ≠ linked origin
  Relocation is performed by loader

## Slide 12: Program relocation (cont..)
We assume here that loaders do not perform relocation
Hence, load origin = linked origin
Called absolute loaders

## Slide 13: Performing relocation
Let
  Translated origin = t_originP
  Linked origin = l_originP
  Symbol = symb in P
  Translation time address = tsymb
  Linked time address = lsymb
Relocation factor of P
  relocation_factorP = l_originP - t_originP (eqn 1)

## Slide 14: Performing relocation (cont..)
Statement which uses symb as operand
Translator puts address tsymb in instruction generated for it
  tsymb = t_originP + dsymb
dsymb = offset of symb in P
  lsymb = l_originP + dsymb

## Slide 15: Performing relocation (cont..)
Now Using eqn 1,
  relocation_factorP = l_originP - t_originP
  lsymb = t_originP + relocation_factorP + dsymb
  lsymb = t_originP + dsymb + relocation_factorP
  lsymb = tsymb + relocation_factorP (eqn 2)
Let IRRP = set of instructions requiring relocation in P

## Slide 16: Performing relocation (cont..)
Following eqn 2, relocation of program P can be performed by
  computing the relocation factor of P and
  adding it to the translated time address (es) in every instruction i Є IRRP

## Slide 17: Linking
Suppose we have application AP consisting of set of program units SP={Pi}
A program unit Pi interacts with another program unit Pj by using addresses of Pj’s instructions and data in its own instructions
To realize such interactions, Pj and Pi must contain public definitions and external references
  Public definition : a symbol pub_symb defined in program unit which may be referenced in other program units
  External references : reference to a symbol ext_symb which is not defined in program unit containing reference

## Slide 18: EXTRN and ENTRY statements
ENTRY :
  List the public definitions of program unit
  Lists those symbols defined in program unit which may be referenced in other program units
EXTRN :
  Lists the symbols to which external references are made in program unit

## Slide 19: Resolving external references
Before AP can be executed, it is necessary that for each Pi in SP, every external reference in Pi should be bound to the correct link time address
Linking is the process of binding an external reference to the correct link time address
An external reference is said to be unresolved until linking is performed for it
Resolved when its linking is completed

## Slide 20: Binary programs
A binary program is a machine language program comprising a set of program units SP s.t. Pi Є SP
  Pi has been relocated to the memory area starting at its link origin
  Linking has been performed for each external reference in Pi

## Slide 21
To form a binary program from a set of object modules, the programmer invokes the linker using the command
linker <link origin>, <object module names> [,<execution start address>]
<link origin> is memory address to be given to first word of binary program
<execution start address> is a pair (program unit name, offset in program unit)

## Slide 22
Linker converts this into linked start address
Stored along with binary program for use when program is to be executed
If specification of <execution start address> is omitted, the execution start address is assumed to be same as linked origin
Linker converts object modules in the set of program units SP into binary program
We have assumed link address = load address, loader simply loads binary program into appropriate area of memory for execution

## Slide 23: Object module
Contains all info necessary to relocate and link program with other programs
Consists four components
  Header : contains translated origin, size and execution start address of P
  Program : contains machine language program corresponding to P
  Relocation table : (RELOCTAB) describes IRRP. Each RELOCTAB entry contains a single field
    Translated address : Translated address of address sensitive instruction

## Slide 24
  Linking table (LINKTAB) : contains info concerning public definitions and external references in P. Each LINKTAB entry contains 3 fields
    Symbol : symbolic name
    Type : PD/EXT indicating whether public definition or external references
    Translated address : For public definition, this is address of first memory word allocated to symbol. For external reference, it is address of memory word which is required to contain the address of symbol

## Slide 25: Self – relocating programs
The manner in which a program can be modified, or can modify itself, to execute from a given load origin can be used to classify programs as follows:
  Non relocatable programs
  Relocatable programs
  Self relocating programs

## Slide 26
Non relocatable programs
  Cannot be executed in any memory area other than the area starting on its translated origin
  Result of address sensitivity of a program
  Eg. Hand coded machine language program
Relocatable programs
  Processed to relocate program to a desired area of memory
  Eg. Object module

## Slide 27
Self relocating programs
  Can perform relocation of its own address sensitive instructions
  Two provisions
    Table of information concerning the address sensitive instructions exists as a part of the program
    Code to perform relocation of address sensitive instructions – called relocating logic

## Slide 28
  Start address of relocating logic is the execution start address of the program
  Relocation logic gains control when program is loaded in memory for execution
  Uses loaded address and information concerning address sensitive instructions to perform its own relocation
  The execution control is now transferred to the relocated program
  A self relocating program can execute in any area of memory